## Slide 1: Satellite Launch Systems
A STEM into Action resource
funded by the UK Space Agency
  In the context of constructing and launching their own model rockets, pupils develop their understanding of how satellites are launched, the economics and the increasing role of private industry in launching satellites
Notes: These materials are aimed at teachers of STEM subjects in secondary schools.
Funding and support was provided by the UK Space Agency.
Development of materials was managed by the Design and Technology Association
Image: Sputnik 1, the first artificial Earth satellite launched by The Soviet Union on Oct. 4, 1957.

## Slide 2: Outcomes
Improve pupils’ understanding of satellite launch systems through:
  Increased awareness of satellites and satellite launch systems
  Learning how satellite launch systems work and operate
  Understanding the design and manufacture of launch systems
  Understanding the economics of satellite launch systems
  Building, launching and testing model rockets
  Re-designing model rockets to improve their performance
STEM
Notes: The project booklet guides pupils through a series of exercises that:
Improve pupils’ understanding of satellites launch systems through building and testing model rockets.

## Slide 3: Working in teams – age 11-14
By working through this section, pupils will become more aware of satellite launch systems and how they are designed, manufactured and operated.
http://www.esa.int/Education/ESA_Academy/Turn_your_ideas_into_satellite_concepts_with_the_ESA_Academy
STEM

## Slide 4: Newton’s laws of motion
Isaac Newton was the first scientist to describe how objects move in the three laws of motion that were named after him
We will be using Newton’s three laws to understand how rockets work
https://en.wikipedia.org/wiki/Isaac_Newton
STEM
Notes: Rockets launched from earth have mass and their propulsion systems must overcome the forces of gravity acting on that mass during launch. Isaac Newton was the first scientist to describe how objects move in the three laws of motion that are now named after him.
We will be using Newton’s three laws (not in their numbered order) to explain how rockets work.

## Slide 5: Newton’s first law
Objects at rest will stay at rest and objects in motion will stay in motion in a straight line unless acted upon by an unbalanced force
Gravity acts on mass with the force acting downwards
Launch pad provides the same upward reaction force
Forces are balanced
STEM
Notes: A rocket on the launch pad is ‘at rest’ because the forces acting on it balance out.
The weight of a rocket is made up of gravity acting on the mass. This weight acts downwards through the feet of the rocket.
Before lift-off, the launch pad provides the same forces acting upwards to balance the weight of the rocket.

## Slide 6: Newton’s third law
For every action there is an equal and opposite reaction
Hot gases from the rocket motor escape downwards at high speed
The rocket motor applies an equal and opposite force upwards on the rocket
STEM
Notes: When the rocket motor ignites, expanding hot gases escape downwards at high speed creating an equal and opposite force upwards on the rocket.

## Slide 7: Newton’s second law
Force = the change in momentum (mV) over time. For a constant mass, force =mass x acceleration. F=ma.
The force from the rocket motor is greater than the force of gravity acting downwards on the mass of the rocket.
With excess force acting upwards, the rocket will accelerate, increasing in velocity and height.
STEM
Notes: In this diagram, the force on the rocket from the motor is greater than the force of gravity acting downwards on the mass of the rocket.
With a constant excess force acting upwards, the rocket will accelerate, increasing in velocity and height.

## Slide 8: Rocket flight profile
Launch
  Rocket thrust – acceleration
Motor burn-out
  Coasting flight – deceleration
Parachute deploys
  Controlled descent – terminal velocity
  Touchdown
STEM
Notes: Later in this guide you will build and test model rockets. The flight profile has three distinct phases with events in-between.
Launch
  Rocket thrust – acceleration
Motor burn-out
  Coasting flight – deceleration
Parachute deploys
  Controlled descent – terminal velocity
  Touchdown
Later you will use an understanding of the science and mathematics to calculate the motion of a rocket to the highest altitude which is called apogee.
Diagram from Estes online curriculum: https://www.estesrockets.com/

## Slide 9: Rocket fuel load
Fuel > 50% of rocket mass at launch
Fuel burn significantly reduces rocket mass during flight, increasing velocity and acceleration
http://www.esa.int
STEM
Notes: The mass of fuel in commercial rockets at launch can be more than 50% of the total mass of the rocket waiting for launch.
Fuel burn after launch reduces the rocket mass and must be considered when calculating the velocity and acceleration.
The mass of solid fuel in model rockets is a very small compared with the mass of the rocket so a reduction in mass due to fuel use can be ignored in our calculations.

## Slide 10: Satellite launch systems
China – Kuaizhou, Long March
Japan – H-II
Europe – Arianne
India – PSLV, GSLV
New Zealand/USA – Electron
Soviet Union – Kosmos, Soyuz
USA – Atlas, Delta, Falcon, Blue Origin
Research total payload and the type(s) of satellites launched by these systems
https://www.rocketlabusa.com/gallery/
STEM
Notes: Due to the huge costs involved, satellite launches were pioneered by governments, with the Soviet Union launching the first artificial Earth satellite called ‘Sputnik’ on 4th October 1957.
Since then, many countries have developed satellite launch capabilities often using modified missiles as the starting point.
More recently, private companies have begun developing commercial satellite launch systems.
The countries, companies and organisations with significant satellite launch capability are listed on this slide.
Some of the private companies, including Rocket Lab in New Zealand with their Electron rocket, are in the early stages of development. Others like Falcon have successfully launched many satellites.

## Slide 11: Alternative launch systems – Balloon
Removes the need for fuel to lift the rocket from Earth into the upper atmosphere
Zero2infinity – Bloostar
JP Aerospace – Airship to Orbit
Research total payload and types of satellite carried
Record your findings in:
Satellite launch systems.xlsx
STEM
Notes: Launch from beneath a balloon in the upper atmosphere (40km altitude) removes the need for rocket fuel to lift the rocket from the ground to the height of the balloon.
Propulsion is only needed to lift the payload to orbit and accelerate to orbital velocity. Companies developing balloon launch systems include: Zero2infinity http://www.zero2infinity.space/ and JP Aerospace http://www.jpaerospace.com/
Pupils can record their research findings in the Excel file Satellite launch systems.xlsx

## Slide 12: Alternative launch systems – Air launch
An aircraft carries the rocket to 15km altitude for launch
Orbital ATK – Pegasus
Virgin Orbit – LauncherOne
Stratolaunch Systems
Research total payload and types of satellite carried
Record your findings in:
Satellite launch systems.xlsx
STEM
Notes: Similar in approach to balloon launch, air launch carries the launcher to altitude (15km) beneath an aircraft.
Launch from an aircraft also has the advantage of starting at the velocity of the launch aircraft.
Pupils can record their research findings in the Excel file Satellite launch systems.xlsx

## Slide 13: Alternative launch systems – Runway
Single stage to orbit
Air breathing rocket
Reaction Engines – Skylon
Research total payload and types of satellite carried
Record your findings in:
Satellite launch systems.xlsx
Create a presentation of your findings
STEM
Notes: As early as the 1980s Rolls Royce and British Aerospace were developing a single stage to orbit, reusable satellite launch system called HOTOL.
Based on a revolutionary ‘air breathing’ rocket engine HOTOL would significantly reduce the amount of fuel needed.
In groups, use the internet to research the total payload with each of the above systems. If the information is available, list the different types of satellites the system is able to launch.
Enter the results of your research into the additional tabs in the spreadsheet used for the previous activity in Satellite launch systems.xlsx
In groups, using the results of your research so far, create a presentation outlining the range of satellite launch systems available, focusing on the payload capacity and environmental impact.
This article may help pupils with their comparisons of launch systems.

## Slide 14: Rocket kits
Estes – One of the largest manufacturers of model rockets to schools
HQ – Colorado, USA
Research data for the rocket and motor you will be using
    Mass of the complete rocket
    Average force from rocket motor
    Duration of rocket motor thrust
http://www2.estesrockets.com/cgi-bin/wedu001P.pgm?p=publicat
STEM
Notes: Use the link on the slide to find data on the rocket kit and rocket motor you will be using.
If you are using an alternative supplier, they should be able to supply similar data on their products.
The UK supplier for Estes products is LogicRC: https://www.logicrc.com/default.aspx?s=c:0,c:D
The information you are searching for is:
Mass of the complete rocket
Average force from rocket motor
Duration of rocket motor thrust
Before and during the build, your group records the information listed in the next section.
Data from the first flight will be used as a benchmark for costing a series of flights.

## Slide 15: Rocket build
In groups, follow the build instructions for your rocket
Work as accurately as you can
Data from different groups will be averaged to reduce errors
Data for the first flight will be used as a benchmark for further flights
Record information before and during the build and for each rocket flight
STEM
Notes: For the rocket build activities, we recommend using these Estes packs:
Viking bulk back of 12 - £59.99 - https://www.logicrc.com/?s=c:0,c:D,c:D050&ItemId=D-ES1755
Launch controller & launch pad - £24.99 - https://www.logicrc.com/?s=c:0,s:launch%20pad,c:D,c:D120&ItemId=D-ES2222
Rocket motors A8-3 pack of 24 - £55 - https://www.logicrc.com/?s=c:0,s:a8-3,c:D,c:D111&ItemId=D-ES1781
Also available from www.modelrockets.co.uk

## Slide 16: Rocket costings – Materials
Cost all the materials used to make your rocket
Example
Rocket kit = £6.75 Rocket motor = £3.20 Glue = £0.30 Abrasive paper = £0.25 Decals = £1.15 Paint = £0.45 Total = £12.10
STEM
Notes: Before starting, pupils should cost all the materials needed to build their rocket.
Make sure they include the cost of all consumable materials like glue, abrasive paper, decals, wadding, etc.

## Slide 17: Rocket costings – Labour
Record the total time your group takes to construct the model rocket
Decide on labour costs per hour
Consider any national minimum wage for your age group
Example
Phil = 0.4 hours Linda = 0.45 hours Tim = 0.35 hours Total = 1.2 hours
STEM
Notes: Groups should record the time it takes to construct their rocket.
As a class decide on labour cost per hour considering any national minimum wage for the age group.

## Slide 18: Rocket costings – Totals
Combine material and labour costs
Agree a profit margin
Compare your costings with other groups
How competitive is your group?
Example
Hourly rate = £5.30 x 1.2 hours = £6.36
Materials = £12.10 Labour = £6.36 Profit @15% = £2.77 Total = £21.23
STEM
Notes: Combine the material and labour costs to calculate the total cost of their rocket including any profit margin.
Groups compare their costings with other groups in the class.
Ask groups, “If you were pitching against other groups in your class, how competitive are you?”
Get groups to compare the published mass of the rocket with the actual mass of their models and those built by other groups. Are there major differences? If so, what might be the cause?

## Slide 19: Rocket testing
Scientists design and perform experiments and analyse the data they collect
Designing repeatable experiments is vital to gaining reliable data
Variables must be controlled and recorded
Scientists focus on explaining changes, making comparisons and looking for patterns
Ariane rocket motor test
STEM
Notes: Scientists spend most of their time designing and performing experiments and analysing the data they collect.
Designing experiments that are repeatable is vital and key to this is carefully controlling and recording variables.
Experiments conducted in this way are repeatable and more likely to produce reliable data.
With reliable data, scientists can focus on making comparisons, looking for patterns and explaining changes.

## Slide 20: Rocket testing – Variables
First flights of same design
Similar weather conditions
The same launch tower
The same location
The same specification rocket motor
List all variables under these headings:
Control variables
Independent variable
Dependent variable
STEM
Notes: For the first set of flights, the rockets are all the same design. The only variations in performance should come from the way they were constructed.
Rockets should be tested on the same day so that weather conditions are the same for all rockets.
All groups will need to use the same launch tower in the same position and the same power of rocket motor.
List all variables under these headings:
Control variables
Weather, design, rocket motor power, launch platform.
Independent variable
Variations in rocket construction.
Dependent variable
Maximum height (apogee) Duration of the flight.

## Slide 21: Rocket testing – Flight times
Use a stop watch with lap counter to record the flight times to:
Motor burn-out – when the solid fuel is used up and the motor is no longer providing thrust.
Highest point or apogee.
  Where possible two people should record each variable with the results being averaged to reduce the impact of factors like individual reaction times.
STEM
Notes: A spreadsheet has been created for your group to record the results from the rocket launches.
Rocket test results.xlsx
The lap counter function on stop watches will let you record the flight times to:
Motor burn-out. The solid fuel is used up and the motor no longer providing thrust.
Highest point or apogee.
Where possible two people should record each variable with the results being averaged to reduce the impact of factors like individual reaction times.

## Slide 22: Rocket testing – Recording angles
Clinometer
Two observers
  Burn-out
  Apogee
Circa 100 metres from the launch pad
STEM
Notes: A clinometer is a simple way of recording the angle of the rocket in the sky. These can be purchased or made in school.
This one was made from a protractor, drinking straw, string and metal washer.
For each rocket flight, two observers with clinometers should take readings. The first should record the angle when the motor burns out and the other when the rocket reaches maximum height.
The observer stands a carefully measured distance from the launch pad. If space allows, this should be the estimated height at apogee. For small rockets with A8-3 motors a distance of 100-150 metres is a good starting point.
Sight along the top of the clinometer allowing the string or pendulum to hang vertically.

## Slide 23: Rocket testing – Calculating height 1
Example – Height from observer
Tan a = opposite adjacent Tan 25 = _h_ 200
0.47 = _h_ 200
0.47 x 200 = h
94 metres = h
STEM
Notes: With these measurements and some maths, we can calculate the height from the observer.

## Slide 24: Rocket testing – Calculating height 2
Add height of observer to find the height above ground
Using the data you collected for your rocket launch, carry out these calculations to find the height at motor burn out and apogee
Example
94 m + 1.7 m = 95.7 m
Apogee = 95.7 m
STEM
Notes: Adding the height of the observer gives us the apogee of the rocket measured from the ground.
Carry out these calculations using the data you collected to find the height at motor burn out and apogee for your rocket.

## Slide 25: Rocket data and performance
Mass of the complete rocket
Specification of rocket motor
  Average force from rocket motor
  Duration of rocket motor thrust
  Specific impulse for rocket motor
Height at motor burn out
Maximum height (apogee)
http://www2.estesrockets.com/cgi-bin/wedu001P.pgm?p=publicat
STEM

## Slide 26: Rocket re-use
The cost of space launches is falling due to:
  Changes in design, materials and manufacturing
  Reusable rockets
SpaceX – Falcon 9
  Significant number of successful launches including: military and supply missions to the International Space Station (ISS)
SpaceX - Dragon capsule docked with the International Space Station
STEM
Notes: Reduced cost of design and manufacture and reusable systems have significantly reduced the cost of satellite launches.
SpaceX is at the forefront of reusable launches with their Falcon 9 system. Falcon 9 has already launched military and commercial satellites plus supply missions to the International Space Station.

## Slide 27: Falcon heavy test launch
SpaceX Falcon Heavy
First launch Feb 6th 2018
Tesla Roadster first payload
Returned two of the three rocket cores safely to Earth for re-use
Payload capacity more than 60 metric tons to orbit
https://www.youtube.com/watch?v=wbSwFU6tY1c
STEM
Notes: Early in 2018 SpaceX launched their first Falcon Heavy and successfully returned two of three rocket cores to Earth for re-use.
Click the link to watch a video of the SpaceX Falcon Heavy launch.

## Slide 28: Refurbished rockets
Model rockets are designed to be flown several times
Make any repairs needed recording all materials and time
Launch your rocket recording the same flight data
Compare the two flights
Has performance been affected?
STEM
Notes: Just like SpaceX Falcon rockets, model rockets are designed to fly a number of times but may need some repairs to refurbish them for the next flight.
In your groups make any repairs on your rocket, making sure you record all of the materials and time it takes to get the rocket ready for its next flight.
Add as little extra material as possible to keep the mass of your rocket to a minimum.
Launch your refurbished rocket with the same specification of rocket motor, recording the same data as before.
Compare the data from the second flight with the data from the first.
Assess whether the performance has been affected and, if so, by how much.
You will use this information in the costing exercise that follows.
Image: public domain

## Slide 29: Costing refurbished flights
Cost the second flight
With no kit to buy, it should be cheaper than the first
Example – Materials
Rocket motor = £3.20 Glue = £0.10 Abrasive paper = £0.20 Total = £3.50
Example – Labour
Phil = 0.1 hours Linda = 0.1.5 hours Tim = 0.1 hours Total = 0.35 hours
STEM
Notes: In this section your groups will calculate the cost of refurbishing your rocket and use this to plan and cost a sequence of flights using your re-usable launch system.
Without the need to buy another rocket kit, the second launch should be cheaper than the first.
Based on the amount of damage and work you had to do to get your rocket flight ready, predict how many flights your rocket might reliably complete. This might be as few as five or many more.
Extrapolate is a term used to describe predicting what will happen assuming conditions remain consistent.

## Slide 30: Costing rocket re-use
Predict how many flights your rocket might reliably complete
Calculate the total costs for all flights
Calculate the average cost of each flight
Decide whether you will charge a premium for a new rocket
Example – Cost for one extra flight
Materials = £3.50 Labour = £1.86 Profit 15% = £0.80 Total = £6.16
Example – Costs for eight launches
First launch = £21.23 7 x refurb’ = £43.12 Total = £64.35
Example – Average launch cost
Divide by 8 = £64.35
Single flight cost = £8.04
STEM
Notes: Teacher collates the results from groups and calculates the average cost across the class.
The more successful launches and recoveries each rocket completes, the cheaper you can offer future flights to potential customers but remember, a failure will be costly and make customers cautious of opting for your launch system.
Using your predicted programme of flights, calculate the total cost of the launches.
Choose whether to modify this based on the class averages.
Now calculate your average launch cost.

## Slide 31: Rocket mass
Weigh your rocket
  Accurate scales
Computer model – Mass analysis
  Accurate shapes
  Material properties for all parts including density
Autodesk Inventor - iProperties
STEM
Notes: If your rocket is already built, it is a simple matter to weigh the physical rocket.
Science departments will have sensitive scales and balances.
Alternatively, you could use kitchen scales but check they are accurate for measurements between 0-100 grams.
Computer model – Mass analysis
In this section you will open a 3D parametric model of a rocket in Autodesk Inventor and run analyses and physics simulations for a rocket flight.
Step-by-step instructions are in the pupil booklet.
Note: CAD analyses will only return an accurate result if the model is fully defined.
Mass analysis
The CAD model in the next task has had material properties assigned to every part in the model. If you model your own rocket using CAD, you must do this yourself.

## Slide 32: Computer analysis - Rocket mass
Parametric = numerical values to control the model
Mass analysis uses density and volume of parts
Volumes added together for assemblies
Add the mass of adhesive, paint, decals, etc.
STEM
Notes: The word ‘parametric’ in the context of modern CAD software refers to the dimensions and numerical values used to define every aspect of a 3D computer model.
In this analysis, Inventor used the density assigned to each part and the volume of the shape to work out its mass.
The software then added the mass of the individual parts together to report the total mass of the rocket assembly.
The motor is a purchased item and made up of several parts including solid fuel, wadding, outer case, dividers, etc.
Bought in components can be modelled as detailed assemblies or as an accurate external shape with the correct mass and centre of gravity entered manually.
Note: You may have to increase the mass of your rocket by a small amount to allow for adhesive, paint, decals, etc. which are not represented in the CAD model.

## Slide 33: Computer analysis – motion simulation
Computer model ‘understands’ mass and inertia
Connections between parts control movement – cylindrical
Model must be properly defined
  Shapes, dimensions, density, gravity, freedom to move
STEM
Notes: The rocket flight simulation uses the mechanism assembly tools and motion analysis tools in Inventor.
Movement of the rocket vertically from the launch pad is controlled using a cylindrical connection allowing the rocket to rise vertically and rotate around the metal rod.
For Inventor to carry out a dynamic motion analysis a number of parameters in the model must be defined accurately including:
Accurate dimensions.
Accurate shapes.
Material properties including density applied to all parts.
Gravity defined including magnitude and direction.

## Slide 34: Computer analysis – Motion simulation
Run the analysis to generate motion data
Graph parameters
  Height v time
  Motor thrust v time
Play the analysis
Interpret the model and graphs
Could the analysis be improved?
STEM
Notes: Step by step instructions are in the pupil guide.
Creating a motion like this from scratch involves advanced CAD techniques and considerable experience using the software.
CAD simulations available to schools cannot currently combine wind tunnel testing (CFD) and dynamic physics (motion) in the same simulation.
Teacher: The main factor missing from the simulation is air resistance. If pupils don’t come up with this you should introduce it. Air resistance is covered in more detail in the 14-19 section of this guide.

## Slide 35: Rocket design and manufacture
Rocket code!
Lighter, stronger, more aerodynamic, ease of repair
Alternative materials or manufacturing
Model on CAD (mass analysis)
Build and test your rocket
Report on performance
https://www.youtube.com/watch?v=-rII1Ky2rj8
STEM
Notes: UK Rocketry Association - Rocket Code http://www.ukra.org.uk/shortsafetycode
The small solid rockets are mostly made from card and balsa wood with plastic nose cones. Although card is light and easy to work, it is easily damaged in impacts and by water.
Important: At all times remember, you must follow the rocket code which does not allow hard, rigid materials that could cause injury. http://www.ukra.org.uk/shortsafetycode
Investigate alternative materials and the manufacturing processes available in your school which may include fabrication, CNC machining and 3D printing.
In groups, develop proposals for a lighter design of rocket with the aim of improving performance.
Model your designs on 3D CAD and use the analysis tools to quantify any mass savings.
Build and test your new design to find out the effect your design changes have had on flight performance.
Teacher: Key performance considerations are total mass and having a streamlined shape. This is where pupils should focus their research and design changes.
There are plenty of web sites explaining streamlining and air resistance.
Choosing lightweight materials is complex because strength is equally important with factors such as strength to weight ratio, cost, availability and ease of manufacture to be considered.

## Slide 36: Satellite launch systems – age 14+
Reference guide
Aimed at pupils engaged in extended projects
Suggestions and links for further investigation and study
Rocket design
Payload design
Data capture
Data processing
STEM
Notes: Introduction
So far these materials have guided you through building, flying and gathering data about the performance of model rockets. You will also be more aware of satellite launch systems and how dynamic computer simulations can accurately simulate rocket flights.
This section of this guide explores the science, technology, engineering and mathematics of satellite launch systems in more detail and is intended as a reference for pupils age 14-19 who are engaged in extended projects including those aimed at external academic and vocational qualifications.
Context
No-one who heard the news on 4th October 1957 that Sputnik 1 was orbiting the earth could have imagined the benefits that satellites would bring over sixty years later.
Today there are thousands of satellites orbiting the Earth helping with a huge number of activities including: weather forecasting, land usage, communications, navigation, search and rescue, defence, etc.
Early military satellites had film cameras that needed to be brought back to earth to retrieve the film for processing and analysis. The development of digital imaging and wireless data transmission made it possible for reconnaissance satellites to remain in orbit. Photographs are encoded and transmitted to earth using radio signals.
Modern artificial satellites use a wide variety of sensors, electronics and programmable devices to gather, process, store and transmit information back to earth. Control signals travel in the opposite direction from Earth to the satellite.
Even more fanciful in 1957 would have been the idea that secondary school pupils could get involved in rocketry and data capture and yet, these types of activity are happening in schools across the world.
Design based on understanding
Solid fuel rocket motors
Calculating flight performance
Structure
Aerodynamics
Payload
Control
Manufacture
Computer analyses and simulations
Testing
Data logging

## Slide 37: Design – based on understanding
Iterative process of improvement
Creativity to solve problems
Considering the needs of others
Understanding context and impact
Know about materials, processes and systems
Prototyping, testing and analysis
STEM
Notes: Design is about using creativity and imagination to solve real and relevant problems by considering the needs of others.
It requires a clear understanding of the design context, likely impact of solutions and the materials, process and systems available to create solutions.
Design is an iterative process of improvement based on developing a better understanding of problems, gained from prototyping, testing and analysis.

## Slide 38: Solid fuel rocket motors
Specific Impulse
Force over the duration of the rocket thrust
Area under the thrust/time graph
STEM
Notes: Specific impulse
In order to calculate the first phase of rocket flight you need to know the total impulse from the rocket motor.
Total Impulse is equal to the force over the duration of the rocket thrust.
Total impulse = force x time
Total impulse can be found from the area beneath the curve in a graph
Estes provide force x time graphs for all of their rocket motors.

## Slide 39: Solid fuel rocket motors
Counting squares
An approximation
  Area of one square is 2 x 0.1 = 0.2 Ns
  Total impulse = 13 x 0.2 = 2.6 Ns
Calculus
  Higher maths and beyond this age group
STEM
Notes: There are several ways of calculating the area under the curve.
Counting squares.
Counting the green squares on the graph on the right gives an estimated area of 13 squares.
The area of one square is 2 x 0.1 = 0.2 Ns
Total impulse = 13 x 0.2 = 2.6 Ns
Calculus (integration) requires higher level mathematics and is beyond the scope of this guide.

## Slide 40: Solid fuel rocket motors
Data logging software may have a calculus function
Experiment to measure thrust of a solid fuel rocket motor
STEM
https://www.youtube.com/watch?v=cGzzkOBEAto
Notes: If your data logging software includes calculus functions it will be able to calculate the area under a graph.
A simple experiment with a force sensor and data logging equipment will record the thrust during an engine firing.
The video shows a school in the US performing this type of experiment.
https://www.youtube.com/watch?v=cGzzkOBEAto

## Slide 41: Solid fuel rocket motors
Excel does not have a calculus function
Approximation method shown in the linked video and Excel file:
Rocket motor impulse.xlsx
STEM
http://www.statisticshowto.com/how-to-find-the-area-under-a-curve-in-microsoft-excel/
Notes: Excel – area under a graph
Although Excel doesn’t have calculus functions, it is possible to get an approximation using a technique demonstrated in the linked video and excel file.
http://www.statisticshowto.com/how-to-find-the-area-under-a-curve-in-microsoft-excel/

## Slide 42: Height at motor burn out
Solid fuel is a small % of the total model rocket mass so, F=Ma can be used
Estes Viking rocket
Mass = 23g = 0.023kg
Total impulse = 2.6Ns
STEM
f = ma
2.6 = 0.023 x a
a = 2.6__ 0.023
Acceleration = 113 m sec2
Notes: Acceleration during the thrust phase
The solid fuel in model rockets has a very small mass compared with the total for the entire rocket so, the formula f=ma can be used for acceleration.
The Estes Viking rocket is popular in schools and, including motor, has a mass of 23 grams.
(This is far less than the mass of the CAD model (101 grams) used in the simulation in the first part of this guide.)

## Slide 43: Velocity at motor burnout
Estes A8 engine duration = 0.7 sec
  Vshut-down = acceleration x duration
  113 x 0.7 = 79.13 m sec1
  Vshut-down = 79.13 m sec1
STEM
Notes: To work this out we need to know the duration of the motor thrust. This can be found in the data sheet for the rocket motor.
The thrust from an Estes A8 rocket motor lasts for 0.7 seconds.

## Slide 44: Height or altitude 1
Height uses a local reference Above Ground Level (AGL)
Height varies from place to place
Altitude uses a universal datum Mean Sea Level (MSL)
Altitude is the same everywhere
STEM
Notes: Height is measured from a local reference or datum point.
For your rocket flights that could be the school field.
Altitude is measured from a universal datum, usually mean sea level (MSL).
Because height varies, aircraft fly using altitude so they know how high they are relative to other aircraft.
Pupils can find out the altitude of your school from detailed maps which show contours and spot heights.
https://www.ordnancesurvey.co.uk/
https://www.bing.com/maps

## Slide 45: Height or altitude 2
Spot heights on OS maps
https://www.ordnancesurvey.co.uk/
What is the altitude and height of your school?
Trig points were used for surveying
What does the term trig stand for?
STEM
Notes: To confuse matters, Ordnance Survey in the UK uses Mean Seal Level (MSL) as the reference but calls the measurements on maps ‘heights’.
Teacher: Tri stand for trigonometry which is the method early map makers used to measure the height of key features.

## Slide 46: Maximum height – Apogee
Fuel runs out
Gravity slows the rocket
Velocity zero = Apogee
Rocket falls back to Earth
Knowing altitudes and time
Calculate average velocity to find heights
STEM
Notes: When the rocket motor runs out of fuel, the force of gravity will slow the rocket until the velocity is zero.
At this point the rocket will be at its highest point called apogee.
After this, the rocket will begin falling back to earth.
Knowing the time, mass of the rocket and start and end velocities, we can calculate the distance travelled.
Next we calculate the average velocity.

## Slide 47: Apogee - Calculations
Average velocity
start velocity + end velocity 2
Coasting distance
Average velocity x time
Maximum height (Apogee)
height at burnout + coasting distance
Vaverage = 79.13 + 0 2
Average velocity = 39. 57 m/s
39.57 x 2.1 Coasting distance = 83.1 metres
27.7 + 83.1 = 110.8 m Apogee = 110.8 metres
STEM
Notes: I order to calculate apogee, we must first calculate average velocity.
Once we know average velocity we can calculate coasting distance.
Adding height at burnout and coasting distance gives us apogee.

## Slide 48: Rocket structures
Light and strong shape needed
Monocoque or shell
  Smooth aerodynamic shape and
  Mounting points for components
Motor mount and nose
  Closes the ends and stiffens the tube
STEM
Notes: Most commercial and model rockets use a monocoque or shell structure where the outer skin, as well as creating a smooth aerodynamic shape, also provides mounting points for the motor, payload and tether for the recovery parachute. Using a monocoque for two purposes like this creates a light yet strong shape.
This partial cutaway shows the disks holding the motor. These are glued into the fuselage tube maintaining the circular section.
As well as parting the air, the nose also maintains the circular section at the top of the fuselage.

## Slide 49: Materials
Strong, light, low cost, safe to work
Fuselage – cardboard
Fins – balsa wood, plywood, aluminium
Nose – balsa wood, polymer
STEM
Notes: The main requirements for materials used to make rockets are:
Strong
Light
Low cost
Safe to cut and shape
Fuselage – Cardboard meets all of these criteria but other materials may provide advantages for your specific design.
Fins – On smaller rockets, card or balsa wood is often used for the fins. Larger rockets might use plywood or even aluminium.
Nose – Balsa wood is very light and easily shaped with a smooth surface, meeting all of the requirements for the nose of a rocket. Commercial kits often include a moulded plastic nose. The process of blow moulding is ideally suited to large volume manufacture.

## Slide 50: Aerodynamics – Frontal area
Air resistance
  We notice air most when the wind is blowing
  Hold a board – flat to a breeze
  Hold a board edge to a breeze
Frontal area
  The hole an object makes in the air
  Measure the CAD model
STEM
Notes: Air resistance – Air is all around us and essential to life, providing the oxygen our bodies need. We notice air when the wind is blowing or when we are moving quickly.
To feel the effect of air resistance, try holding a large sheet of plywood in front of you facing into the wind. Try again with the board edge to the wind. Was it harder or easier to hold the board?
Frontal area – The hole objects make when they move through the air is a key part of drag. Anything you can do to reduce the frontal area of your rocket will help reduce the air resistance.
CAD model – A work plane and sketch have been created and the rocket outline projected/drawn onto the sketch. The Inspect > Area tool in Inventor will measure and display the area of a closed outline.

## Slide 51: Aerodynamics – Drag
Air resists movement
Objects moving through air
Coefficient of drag (0-1 Cd)
  Skin friction
  Form drag
Experiment with CAD shapes
Hummer Cd = 0.57
VW XL1 Cd= 0.19
(https://phys.org/)
https://knowledge.autodesk.com/support/flow-design/learn-explore/caas/CloudHelp/cloudhelp/ENU/FlowDesign/files/GUID-8D9B9515-FB68-4FA5-A514-D63EF545A00E-htm.html
STEM
Notes: The effect of air resisting movement is called drag.
Scientists devised a way of measuring it called the coefficient of drag which is used extensively for cars.
A number between 0 and 1 with the symbol Cd
Two cars at the opposite ends of aerodynamic efficiency are shown with their drag coefficients.
Shapes have been provided in Autodesk for pupils to test using the Flow Design tools.

## Slide 52: Aerodynamics – High speeds
Military jet flying in humid air
Low pressure causes moisture to condense for a split second
Thrust SSC land speed record car – 763 mph
Shock wave disturbing dust on lake bed
Aerodynamics is part of fluidics. A part of engineering and requires high level mathematics
http://www.bbc.com/future/story/20160216-you-think-this-is-a-sonic-boom-its-not
http://www.bloodhoundssc.com/news/speed-sound-0
STEM
Notes: Drag must be taken into consideration when calculating rocket performance.
The top photograph shows a military jet flying in very humid air. Low pressure around the aircraft causes the moisture in the atmosphere to condense forming water droplets for a split second before evaporating back into water vapour.
Unusual weather allows us to see the pressure differences around the aircraft.
The lower photograph was taken from a microlight and shows Thrust SSC on one of its land speed record breaking runs. At supersonic speed the car created a shockwave which can clearly be seen as a disturbance in the dust on the ground. The shockwave is travelling across the desert at the same speed as the car, 763 mph!
The study of how fluids, including air, behave is called fluidics and involves high level mathematics. Fluidics forms part of undergraduate engineering courses at university.

## Slide 53: Aerodynamics – CFD
Computational Fluid Dynamics
Flow lines around the rocket
Stable airflow 150 m/s
Blue lines airflow of 0 m/s
Red lines airflow of 200 m/s
How to use flow lines – YouTube
Flow Design drag plot – YouTube
STEM
Notes: Computational fluid dynamics (CFD) tools can be found in most 3D parametric 3D modelling software including Autodesk Inventor.
The top image shows an Autodesk Inventor Flow Design analysis of the air travelling past a model rocket. In the simulation, the air speed was set to 150 m sec1. The blue lines show air travelling at 0 m sec1 while red lines show air travelling at 200 m/s.
The graph is a drag plot from Inventor. It is reporting a drag coefficient of 0.329 Cd and drag force of 6.3 N.
Several parametric CAD programs are available free to schools and pupils at home including Autodesk Inventor, which was used to create these materials.
How to use flow lines – YouTube
Flow Design drag plot – YouTube

## Slide 54: Aerodynamics – Wind tunnel
Wind tunnels predate computer analysis
NASA Ames Research Centre
Model Space Launch System
Pressure sensitive paint
Credit: NASA/Dominic Hart
https://phys.org/news/2017-01-fluctuating-flight-captured-high-tech.html#jCp
STEM
Notes: Before the invention of computers, engineers used wind tunnels to observe the behaviour of air passing over physical objects.
Here, Amber Favaregh of NASA’s Langley Research Center prepares a model of the Space Launch System rocket. She is using pressure-sensitive paint in a wind tunnel at NASA's Ames Research Center.

## Slide 55: Aerodynamics – Wind tunnel
Simple wind tunnel for testing scale models
NASA published a very useful guide for schools
Rocket wind tunnel – NASA
STEM
Notes: It is relatively simple to design and build a wind tunnel for testing small objects and scale models.
NASA published a very useful guide for schools.
Rocket wind tunnel – NASA

## Slide 56: Payload rockets
Estes payload rockets
  Loadstar II
  Eggscaliber
Instructable
  Side facing keyring camera
STEM
Notes: There are several designs of payload rocket available including ones with space for an egg to see if it can survive the flight intact and others that carry a small camera taking pictures or video during the flight.
These can form the basis of projects where pupils design and make modifications to kit rockets to carry out specific tasks.
Estes – Loadstar II and Eggscaliber
The Instructable shows how to modify an Estes Reflector rocket to accommodate a keyring camera looking sideways.
http://www.instructables.com/id/Model-Rocket-with-horizontal-HD-video-keychain-cam/

## Slide 57: Live payloads
The International Space Station is permanently occupied
Astronauts consent to flying
What are the ethics of using living creatures in experiments?
STEM
Notes: Pupils way consider using living creatures in your rocket experiments.
Before they do, explore with them the ethics of using creatures that cannot consent to the experiment that may cause them harm.
Image: http://blog.growingwithscience.com/wp-content/uploads/2016/09/Assorted-beetles.jpg

## Slide 58: First animal in space
Sputnik 2 – Nov’ 3rd 1957
Dog Laika
One way trip
https://en.wikipedia.org/wiki/Laika
STEM
Notes: The Soviet Union successfully launched a dog called Laika into space in Sputnik 2 on 3 November 1957.
Re-entry had not been tried so engineers had no way of retrieving Laika alive.
The spacecraft was designed with air supplies for several days but the dog survived only a few hours due to overheating caused by a spacecraft malfunction.
The soviets justified the loss of Laika as the only way of testing spacecraft systems prior to launching the first cosmonaut into space.
The secretive military world of the 1950s was very different to today and attitudes on animals being used in experiments have changed.
https://en.wikipedia.org/wiki/Laika

## Slide 59: Manufacture
Hand – Fuselage
  Rolled card composite
  Trabant – Duraplast composite
  Thermosetting polyester reinforced with cotton or wool
CNC machining – Nose
  Aluminium mould
3D printed – Rocket parts
  ABS or PLA
http://astermachining.com/on-the-bench/
https://www.louwmanmuseum.nl/en/Ontdekken/Ontdek-de-collectie/trabant-601-ls
https://www.thingiverse.com/thing:8754
STEM
Notes: Hand – Fuselage
Manufacturing by hand was covered in the age 11-14 section. You could make your own fuselage by wrapping your own cardboard tubes. Nose cones could be made by hand from papier-mâché, a composite material.
In the Soviet Union, Trabant cars had bodies manufactured from a material called Duroplast. A composite material made from thermosetting resin reinforced with cotton or wool fibres. People joked that the bodies of Trabants were made from papier-mâché!
CNC Machining – Nose mould
Your school may have access to manual or CNC lathes or milling machines. These could be used to make moulds for nose cones or payload/camera bays.
3D printing – Rocket parts
Many schools have 3D printers, a process which allows much more complex shapes to be manufactured.
This set of rocket parts was posted on 3D model download site Thingiverse.
https://www.thingiverse.com/thing:8754

## Slide 60: Computer simulations
Motion physics simulation
Sun, Mercury, Venus, Earth, Mars
PTC Creo Parametric
https://www.ptc.com/en/academic-program/products/free-software solar_system.asm
STEM
Notes: Petter Frieberg, an engineer working for global software company PTC created a motion simulation of the inner four planets using Creo Parametric.
Click on the image to play a video of the simulation.
The Creo suite of software is available free to schools and their pupils for educational use.
https://www.ptc.com/en/academic-program/products/free-software

## Slide 61: Testing
Gather reliable data
Measure performance
Control variables
Careful observation
Accurate measurements
Inform design improvement
STEM
Notes: The purpose of testing is to gather reliable data about the performance of a design to inform decisions about design improvements.
The key to obtaining reliable data is controlling variables and making accurate measurements. This was covered in the 11-14 section at the beginning of this guide.

## Slide 62: Data logging and micro controllers
Arduino
Raspberry Pi
Micro:bit
Crumble
STEM
Notes: Schools are using a wide range of microcontrollers including Arduino which is aimed at the maker and hackspace communities and Raspberry Pi designed specifically for education.
Small, inexpensive programmable devices have been produced for schools who are new to programmable systems.
The BBC in partnership with Microsoft, ARM and other organisations developed the Micro:bit for schools. Aimed at coding classes, the Micro:bit has built-in sensors and an LED array for output.
Micro:bit can be connected to external sensors and output devices through the edge connector but additional electronics are needed to drive devices and protect the Micro:bit.
Crumble is another low-cost, credit card size microcontroller aimed at pupils engaged in D&T projects.
Additional electronics on the Crumble allow it to ‘drive’ DC outputs like motors and protect the board against damage.

## Slide 63: Guidance systems
Passive stability
Centre of gravity in front of centre of pressure
http://www.robotroom.com/Model-Rocket-Launch-Controller.html
Active guidance systems
Programmable
Giros, GPS, etc.
https://www.youtube.com/watch?v=qnUfsLCa8h8
STEM
STEM
Notes: Most model rockets rely on passive stability to make them fly. The centre of gravity and centre of pressure are arranged so that movable control surfaces are not needed to make the rocket fly straight.
However, once the model is launched, it is at the mercy of winds.
http://www.robotroom.com/Model-Rocket-Launch-Controller.html
Serious amateurs are now designing and buildings active control systems using programmable systems and remote control servos.
This Italian rocketeer has successfully flown a rocket with a control system he designed and built.
https://www.youtube.com/watch?v=qnUfsLCa8h8

## Slide 64: Micro satellites
Overall number of satellites has increased
Government agencies
Government spin-offs
Private companies
Scale
  JWST = 6,300 kg
  Pico satellite ± 1 kg
STEM
https://www.economist.com/blogs/dailychart/2011/08/space-industry
Notes: Since the launch of Sputnik 1 in 1957 the number of satellite launches has increased.
Recent years has seen a significant increase in the number of private companies launching satellites.
Some of these like the United Space Alliance are a government spin-off from NASA while SpaceX was set up by Elon Musk of Tesla fame.
https://www.economist.com/blogs/dailychart/2011/08/space-industry
Modern satellites range in size from the James Webb Space Telescope shown on the right with a mass of 6,300 kg right down to pico-satellites with a mass of around 1 kg.

## Slide 65: CubeSat
A standard for pico satellites
  Developed by California Polytechnic State and Stamford Universities
Maximums
  10 x 10 x 10 cm cube
  Maximum1.33 kg
University of Surrey
  At the forefront of UK satellite development since 1979
  Click image for video >>>>
https://www.surrey.ac.uk/surrey-space-centre/missions/strand-1
STEM
Notes: The CubeSat ‘standard’ falls into the top of the pico-satellite category and was developed by the California Polytechnic State and Stamford universities. CubeSats must fit within a cube 10 x 10 x 10 cm cube with a mass of no more than 1.33 kg.
CubeSat has created opportunities for universities, organisations and even schools to design experiments that piggy-back on much larger commercial satellite launches.
The University of Surrey in the UK has been at the forefront of small satellite developments since 1979.
Click on the link below and watch a video explaining the different systems in a CubeSat.
https://www.surrey.ac.uk/surrey-space-centre/missions/strand-1

## Slide 66: CubeSat
February 2017
Indian rocket (PSLV)
104 CubeSats into orbit
Many satellite launchers have modular payloads
https://www.theverge.com/2017/2/14/14601938/india-pslv-rocket-launch-satellites-planet-doves
STEM
Notes: In February 2017 an Indian rocket launched by PSLV carried 104 CubeSats into orbit.
Satellite launch systems are modular allowing satellites of different sizes to be carried in a single launch.
https://www.theverge.com/2017/2/14/14601938/india-pslv-rocket-launch-satellites-planet-doves